Willow Creek Downstream Migrant Trap Site

2007 In-Season Trapping Update –March 16, 2007

Synopsis: The 2007 Downstream Migrant trapping season at the Willow Creek Trap Site (river kilometer 34) is being conducted jointly by the USFWS Arcata Fish and Wildlife Office (AFWO) and the Yurok Tribal Fisheries Program (YTFP) on the mainstem Trinity River near Willow Creek, California.  The site utilizes multiple eight foot diameter rotary screw traps.  The season began March 5, 2007 with the installation of one trap.  A second trap was installed March 15, 2007 and a third trap will be installed the week of March 19th, river flow permitting.

This summary includes data from March 6th, 2007 through March 13th, 2007.

Raw daily catches of Chinook salmon (Oncorhynchus tshawytscha) are steadily increasing (Table 1), and have been captured each day sampling occurred.  All fish captured during this time period are less than 45 mm, and appear to be in good condition. Weekly mean Fulton’s K values are near 1.0.

Raw daily catches of steelhead (Oncorhynchus mykiss) smolts are low (Table 1), but present in the catch.  No steelhead young of the year have been captured this sampling year.  All steelhead smolts captured appear to be in good condition, except for one which had a fungal infection.  One of the steelhead smolts captured was marked with a purple photonic mark from the Hoopa Valley Tribal Fisheries Department trapping operation at the Pear Tree site.  Weekly mean Fulton’s K values are slightly higher than 1.0.

Raw daily catches of coho salmon (Oncorhynchus kisutch) are low (Table 1), but present in the catch.  Only one coho salmon smolt has been captured to date, and it was in good condition with a Fulton’s K value of 1.2.  All coho salmon young-of-the-year appear to be in good condition with weekly mean Fulton’s K values near 1.0.

Table 1.  Raw catch of juvenile salmonids at the Willow Creek downstream migrant trapping site as of March 13, 2007.  NC = no clip.

| Dates | Julian Week | Trap Days | Chinook Age 0 NC | Steelhead Smolts NC | Coho Age 0 | Coho Smolts NC |
| --- | --- | --- | --- | --- | --- | --- |
| 3/5 to 3/11 | 10 | 4 | 27 | 3 | 0 | 0 |
| 3/12 to 3/18 | 11 | 2 | 32 | 5 | 9 | 1 |